## Slide 1
Chapter 5
Digital Design and Computer Architecture: ARM® Edition
Sarah L. Harris and David Money Harris

## Slide 2
Chapter 5 :: Topics
Introduction
Arithmetic Circuits
Number Systems
Sequential Building Blocks
Memory Arrays
Logic Arrays

## Slide 3
Digital building blocks:
  Gates, multiplexers, decoders, registers, arithmetic circuits, counters, memory arrays, logic arrays
Building blocks demonstrate hierarchy, modularity, and regularity:
  Hierarchy of simpler components
  Well-defined interfaces and functions
  Regular structure easily extends to different sizes
Will use these building blocks in Chapter 7 to build microprocessor
Introduction

## Slide 4
1-Bit Adders

## Slide 5
Types of carry propagate adders (CPAs):
  Ripple-carry (slow)
  Carry-lookahead (fast)
  Prefix (faster)
Carry-lookahead and prefix adders faster for large adders but require more hardware
Symbol
Multibit Adders (CPAs)

## Slide 6
Chain 1-bit adders together
Carry ripples through entire chain
Disadvantage: slow
Ripple-Carry Adder

## Slide 7
tripple = NtFA
where tFA is the delay of a 1-bit full adder
Ripple-Carry Adder Delay

## Slide 8
Can we calculate faster?

## Slide 9
Compute Cout for k-bit blocks using generate and propagate signals
Some definitions:
  Column i produces a carry out by either generating a carry out or propagating a carry in to the carry out
  Generate (Gi) and propagate (Pi) signals for each column:
    Generate: Column i will generate a carry out if Ai and Bi are both 1.
  Gi = Ai Bi
    Propagate: Column i will propagate a carry in to the carry out if Ai or Bi is 1.
  Pi = Ai + Bi
    Carry out: The carry out of column i (Ci) is:
  Ci = Ai Bi + (Ai + Bi )Ci-1 = Gi + Pi Ci-1
Carry-Lookahead Adder

## Slide 10
Now use column Propagate and Generate signals to compute Block Propagate and Generate signals for k-bit blocks, i.e.:
  Compute if a k-bit group will propagate a carry in (to the block) to the carry out (of the block)
  Compute if a k-bit group will generate a carry out (of the block)
Block Propagate and Generate

## Slide 11
Example: Block propagate and generate signals for 4-bit blocks (P3:0 and G3:0):
  P3:0 = P3P2 P1P0
  G3:0 = G3 + G2P3 + G1P2P3 + G0P1P2P3
  = G3 + P3 (G2 + P2 (G1 + P1G0 )
Block Propagate and Generate Signals

## Slide 12
In general for a block spanning bits i through j,
  Pi:j = PiPi-1 Pi-2 … Pj
  Gi:j = Gi + Pi (Gi-1 + Pi-1 (Gi-2 + Pi-2 … Gj )
  Ci = Gi:j + Pi:j Cj-1
Block Propagate and Generate Signals

## Slide 13
32-bit CLA with 4-bit Blocks

## Slide 14
Step 1: Compute Gi and Pi for all columns
Step 2: Compute G and P for k-bit blocks
Step 3: Cin propagates through each k-bit propagate/generate logic (meanwhile computing sums)
Step 4: Compute sum for most significant k-bit block
Carry-Lookahead Addition

## Slide 15
Step 1: Compute Gi and Pi for all columns
Carry-Lookahead Addition
  Gi = Ai Bi
  Pi = Ai + Bi

## Slide 16
Step 1: Compute Gi and Pi for all columns
Step 2: Compute G and P for k-bit blocks
Carry-Lookahead Addition
  P3:0 = P3P2 P1P0
  G3:0 = G3 + P3 (G2 + P2 (G1 + P1G0 )

## Slide 17
Step 1: Compute Gi and Pi for all columns
Step 2: Compute G and P for k-bit blocks
Step 3: Cin propagates through each k-bit propagate/generate logic (meanwhile computing sums)
Carry-Lookahead Addition
A
3:0
B
3:0
S
3:0
4-bit CLA
Block
C
in
A
7:4
B
7:4
S
7:4
4-bit CLA
Block
C
3
C
7
A
27:24
B
27:24
S
27:24
4-bit CLA
Block
C
23
A
31:28
B
31:28
S
31:28
4-bit CLA
Block
C
27
C
out
B
0
+
+
+
+
P
3:0
G
3
P
3
G
2
P
2
G
1
P
1
G
0
P
3
P
2
P
1
P
0
G
3:0
C
in
C
out
A
0
S
0
C
0
B
1
A
1
S
1
C
1
B
2
A
2
S
2
C
2
B
3
A
3
S
3
C
in
B
0
+
+
+
+
P
3:0
G
3
P
3
G
2
P
2
G
1
P
1
G
0
P
3
P
2
P
1
P
0
G
3:0
C
in
C
out
A
0
S
0
C
0
B
1
A
1
S
1
C
1
B
2
A
2
S
2
C
2
B
3
A
3
S
3
C
in
B
0
+
+
+
+
P
3:0
G
3
P
3
G
2
P
2
G
1
P
1
G
0
P
3
P
2
P
1
P
0
G
3:0
C
in
C
out
A
0
S
0
C
0
B
1
A
1
S
1
C
1
B
2
A
2
S
2
C
2
B
3
A
3
S
3
C
in
B
0
+
+
+
+
P
3:0
G
3
P
3
G
2
P
2
G
1
P
1
G
0
P
3
P
2
P
1
P
0
G
3:0
C
in
C
out
A
0
S
0
C
0
B
1
A
1
S
1
C
1
B
2
A
2
S
2
C
2
B
3
A
3
S
3
C
in

## Slide 18
Step 1: Compute Gi and Pi for all columns
Step 2: Compute G and P for k-bit blocks
Step 3: Cin propagates through each k-bit propagate/generate logic (meanwhile computing sums)
Step 4: Compute sum for most significant k-bit block
Carry-Lookahead Addition
B
0
+
+
+
+
P
3:0
G
3
P
3
G
2
P
2
G
1
P
1
G
0
P
3
P
2
P
1
P
0
G
3:0
C
in
C
out
A
0
S
0
C
0
B
1
A
1
S
1
C
1
B
2
A
2
S
2
C
2
B
3
A
3
S
3
C
in
B
0
+
+
+
+
P
3:0
G
3
P
3
G
2
P
2
G
1
P
1
G
0
P
3
P
2
P
1
P
0
G
3:0
C
in
C
out
A
0
S
0
C
0
B
1
A
1
S
1
C
1
B
2
A
2
S
2
C
2
B
3
A
3
S
3
C
in
B
0
+
+
+
+
P
3:0
G
3
P
3
G
2
P
2
G
1
P
1
G
0
P
3
P
2
P
1
P
0
G
3:0
C
in
C
out
A
0
S
0
C
0
B
1
A
1
S
1
C
1
B
2
A
2
S
2
C
2
B
3
A
3
S
3
C
in
B
0
+
+
+
+
P
3:0
G
3
P
3
G
2
P
2
G
1
P
1
G
0
P
3
P
2
P
1
P
0
G
3:0
C
in
C
out
A
0
S
0
C
0
B
1
A
1
S
1
C
1
B
2
A
2
S
2
C
2
B
3
A
3
S
3
C
in

## Slide 19
For N-bit CLA with k-bit blocks:
tCLA = tpg + tpg_block + (N/k – 1)tAND_OR + ktFA
  tpg : delay to generate all Pi, Gi
  tpg_block : delay to generate all Pi:j, Gi:j
  tAND_OR : delay from Cin to Cout of final AND/OR gate in k-bit CLA block
An N-bit carry-lookahead adder is generally much faster than a ripple-carry adder for N > 16
Carry-Lookahead Adder Delay

## Slide 20
Computes carry in (Ci-1) for each column, then computes sum:
Si = (Ai ^ Bi) ^ Ci-1
Computes G and P for 1-, 2-, 4-, 8-bit blocks, etc. until all Gi (carry in) known
log2N stages
Prefix Adder

## Slide 21
Carry in either generated in a column or propagated from a previous column.
Column -1 holds Cin, so
  G-1 = Cin
Carry in to column i = carry out of column i-1:
  Ci-1 = Gi-1:-1
Gi-1:-1: generate signal spanning columns i-1 to -1
Sum equation:
  Si = (Ai ^ Bi) ^ Gi-1:-1
Goal: Quickly compute G0:-1, G1:-1, G2:-1, G3:-1, G4:-1, G5:-1, … (called prefixes) (= C0, C1, C2, C3, C4, C5, …)
Prefix Adder

## Slide 22
Generate and propagate signals for a block spanning bits i:j
  Gi:j = Gi:k + Pi:k Gk-1:j
  Pi:j = Pi:kPk-1:j
In words:
  Generate: block i:j will generate a carry if:
    upper part (i:k) generates a carry or
    upper part (i:k) propagates a carry generated in lower part (k-1:j)
  Propagate: block i:j will propagate a carry if both the upper and lower parts propagate the carry
Prefix Adder

## Slide 23
16-Bit Prefix Adder Schematic
0:-1
-1
2:1
1:-1
2:-1
0
1
2
4:3
3
6:5
5:3
6:3
4
5
6
5:-1
6:-1
3:-1
4:-1
8:7
7
10:9
9:7
10:7
8
9
10
12:11
11
14:13
13:11
14:11
12
13
14
13:7
14:7
11:7
12:7
9:-1
10:-1
7:-1
8:-1
13:-1
14:-1
11:-1
12:-1
15
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
G
k-1:j
P
k-1:j
G
i:k
P
i:k
G
i:j
P
i:j
B
i
A
i
G
i:i
P
i:i
i
i:j
B
i
A
i
G
i-1:-1
S
i
i

## Slide 24
tPA = tpg + log2N(tpg_prefix ) + tXOR
  tpg: delay to produce Pi, Gi (AND or OR gate)
  tpg_prefix: delay of black prefix cell (AND-OR gate)
Prefix Adder Delay

## Slide 25
Compare delay of: 32-bit ripple-carry, CLA, and prefix adders
CLA has 4-bit blocks
2-input gate delay = 10 ps; full adder delay = 30 ps
tripple = NtFA = 32(30 ps)
= 960 ps
tCLA = tpg + tpg_block + (N/k – 1)tAND_OR + ktFA
= [10 + 60 + (7)20 + 4(30)] ps
= 330 ps
tPA = tpg + log2N(tpg_prefix ) + tXOR
= [10 + log232(20) + 10] ps
= 120 ps
Adder Delay Comparisons

## Slide 26
// SystemVerilog module adder #(parameter N = 8) (input logic [N–1:0] a, b, input logic cin, output logic [N–1:0] s, output logic cout);
assign {cout, s} = a + b + cin;
endmodule
Adder HDL description

## Slide 27
Subtracter

## Slide 28
Comparator: Equality

## Slide 29
Comparator: Less Than

## Slide 30
module comparator #(parameter N = 8) (input logic [N–1:0] a, b, output logic eq, neq, lt, lte, gt, gte);
assign eq = (a == b); assign neq = (a != b); assign lt = (a < b); assign lte = (a <= b); assign gt = (a > b); assign gte = (a >= b);
endmodule

## Slide 31
A typical ALU should perform:
Addition
Subtraction
AND
OR
ALU: Arithmetic Logic Unit

## Slide 32
ALU in 1950s

## Slide 33
ALU in 1970s: 8008 8-bit, 10um
The Intel 8008 die with key functional blocks labeled.

## Slide 34
ALU: Arithmetic Logic Unit
ALUControl1:0 | Function
00 | Add
01 | Subtract
10 | AND
11 | OR
Example: Perform A + B
ALUControl = 00
Result = A + B

## Slide 35
ALU: Arithmetic Logic Unit
ALUControl1:0 | Function
00 | Add
01 | Subtract
10 | AND
11 | OR
Example: Perform A OR B

## Slide 36
ALU: Arithmetic Logic Unit
ALUControl1:0 | Function
00 | Add
01 | Subtract
10 | AND
11 | OR
Example: Perform A OR B
ALUControl1:0 = 11
Mux selects output of OR gate as Result, so
Result = A OR B

## Slide 37
ALU: Arithmetic Logic Unit
ALUControl1:0 | Function
00 | Add
01 | Subtract
10 | AND
11 | OR
Example: Perform A + B

## Slide 38
ALU: Arithmetic Logic Unit
ALUControl1:0 | Function
00 | Add
01 | Subtract
10 | AND
11 | OR
Example: Perform A + B
ALUControl1:0 = 00
ALUControl0 = 0, so:
Cin to adder = 0
2nd input to adder is B
Mux selects Sum as Result, so
Result = A + B

## Slide 39
Flag | Description
N | Result is Negative
Z | Result is Zero
C | Adder produces Carry out
V | Adder oVerflowed
ALU with Status Flags

## Slide 40
ALU with Status Flags

## Slide 41
ALU with Status Flags: Negative
N = 1 if:
Result is negative
So, N is connected to most significant bit of Result

## Slide 42
ALU with Status Flags: Zero
Z = 1 if:
all of the bits of Result are 0

## Slide 43
ALU with Status Flags: Carry
C = 1 if:
Cout of Adder is 1
AND
ALU is adding or subtracting (ALUControl is 00 or 01)

## Slide 44
ALU with Status Flags: oVerflow
V = 1 if:
The addition of 2 same-signed numbers produces a result with the opposite sign

## Slide 45
ALU with Status Flags: oVerflow
V = 1 if:
ALU is performing addition or subtraction
(ALUControl1 = 0)

## Slide 46
ALU with Status Flags: oVerflow
V = 1 if:
ALU is performing addition or subtraction
(ALUControl1 = 0)
AND
A and Sum have opposite signs

## Slide 47
ALU with Status Flags: oVerflow
V = 1 if:
ALU is performing addition or subtraction
(ALUControl1 = 0)
AND
A and Sum have opposite signs
AND
A and B have same signs upon addition OR
A and B have different signs upon subtraction

## Slide 48
ALU with Status Flags: oVerflow
V = 1 if:
ALU is performing addition or subtraction
(ALUControl1 = 0)
AND
A and Sum have opposite signs
AND
A and B have same signs upon addition (ALUControl0 = 0) OR
A and B have different signs upon subtraction
(ALUControl0 = 1)

## Slide 49
Logical shifter: shifts value to left or right and fills empty spaces with 0’s
  Ex: 11001 >> 2 = 00110
  Ex: 11001 << 2 = 00100
Arithmetic shifter: same as logical shifter, but on right shift, fills empty spaces with the old most significant bit (msb)
  Ex: 11001 >>> 2 = 11110
  Ex: 11001 <<< 2 = 00100
Rotator: rotates bits in a circle, such that bits shifted off one end are shifted into the other end
  Ex: 11001 ROR 2 = 01110
  Ex: 11001 ROL 2 = 00111
Shifters

## Slide 50
Shifter Design
Select bit
Select bit
Control bit
control bit

## Slide 52
A << N = A × 2N
  Example: 00001 << 2 = 00100 (1 × 22 = 4)
  Example: 11101 << 2 = 10100 (-3 × 22 = -12)
A >>> N = A ÷ 2N
  Example: 01000 >>> 2 = 00010 (8 ÷ 22 = 2)
  Example: 10000 >>> 2 = 11100 (-16 ÷ 22 = -4)
Shifters as Multipliers, Dividers

## Slide 53
Partial products formed by multiplying a single digit of the multiplier with multiplicand
Shifted partial products summed to form result
Multipliers

## Slide 54
4 x 4 Multiplier
+

## Slide 55
A/B = Q + R/B
Decimal Example: 2584/15 = 172 R4
Dividers

## Slide 56
A/B = Q + R/B
Decimal Example: 2584/15 = 172 R4
Long-Hand:
Dividers

## Slide 57
A/B = Q + R/B
Decimal Example: 2584/15 = 172 R4
Long-Hand:
Dividers
Long-Hand Revisited:

## Slide 58
A/B = Q + R/B
Decimal: 2584/15 = 172 R4
Dividers
Binary: 1101/0010 = 0110 R1

## Slide 59
Divider Algorithm
A/B = Q + R/B
R’ = 0
for i = N-1 to 0
R = {R’ << 1, Ai}
D = R - B
if D < 0, Qi= 0; R’= R
else Qi= 1; R’= D
R=R’
Binary: 1101/10 = 0110 R1

## Slide 60
4 x 4 Divider
Division: A/B = Q + R/B
R’ = 0
for i = N-1 to 0
R = {R’ << 1, Ai}
D = R - B
if D < 0, Qi=0, R’=R
else Qi=1, R’=D
R=R’
Each row computes one iteration of the division algorithm.

## Slide 61
4 x 4 Divider
Each row computes one iteration of the division algorithm.

## Slide 62
Numbers we can represent using binary representations
  Positive numbers
    Unsigned binary
  Negative numbers
    Two’s complement
    Sign/magnitude numbers
What about fractions?
Number Systems

## Slide 63
Two common notations:
Fixed-point: binary point fixed
Floating-point: binary point floats to the right of the most significant 1
Numbers with Fractions

## Slide 64
6.75 using 4 integer bits and 4 fraction bits:
  Binary point is implied
  The number of integer and fraction bits must be agreed upon beforehand
Fixed-Point Numbers

## Slide 65
Represent 7.510 using 4 integer bits and 4 fraction bits.
  01111000
Fixed-Point Number Example

## Slide 66
Representations:
  Sign/magnitude
  Two’s complement
Example: Represent -7.510 using 4 integer and 4 fraction bits
  Sign/magnitude:
  11111000
  Two’s complement:
  1. +7.5: 01111000
  2. Invert bits: 10000111
  3. Add 1 to lsb: + 1
  10001000
Signed Fixed-Point Numbers

## Slide 67
Binary point floats to the right of the most significant 1
Similar to decimal scientific notation
For example, write 27310 in scientific notation:
  273 = 2.73 × 102
In general, a number is written in scientific notation as:
± M × BE
  M = mantissa
  B = base
  E = exponent
  In the example, M = 2.73, B = 10, and E = 2
Floating-Point Numbers

## Slide 68
Example: represent the value 22810 using a 32-bit floating point representation
We show three versions – final version is called the IEEE 754 floating-point standard
Floating-Point Numbers

## Slide 69
Convert decimal to binary
  22810 = 111001002
Write the number in “binary scientific notation”:
  111001002 = 1.110012 × 27
Fill in each field of the 32-bit floating point number:
  The sign bit is positive (0)
  The 8 exponent bits represent the value 7
  The remaining 23 bits are the mantissa
Floating-Point Representation 1

## Slide 70
First bit of the mantissa is always 1:
  22810 = 111001002 = 1.11001 × 27
So, no need to store it: implicit leading 1
Store just fraction bits in 23-bit field
Floating-Point Representation 2

## Slide 71
Biased exponent: bias = 127 (011111112)
  Biased exponent = bias + exponent
  Exponent of 7 is stored as:
  127 + 7 = 134 = 0x100001102
The IEEE 754 32-bit floating-point representation of 22810
in hexadecimal: 0x43640000
Floating-Point Representation 3

## Slide 72
Write -58.2510 in floating point (IEEE 754)
Floating-Point Example

## Slide 73
Write -58.2510 in floating point (IEEE 754)
Convert decimal to binary:
  58.2510 = 111010.012
Write in binary scientific notation:
1.1101001 × 25
Fill in fields:
  Sign bit: 1 (negative)
  8 exponent bits: (127 + 5) = 132 = 100001002
  23 fraction bits: 110 1001 0000 0000 0000 0000
in hexadecimal: 0xC2690000
Floating-Point Example

## Slide 74
Number | Sign | Exponent | Fraction
0 | X | 00000000 | 00000000000000000000000
∞ | 0 | 11111111 | 00000000000000000000000
- ∞ | 1 | 11111111 | 00000000000000000000000
NaN | X | 11111111 | non-zero
Floating-Point: Special Cases

## Slide 75
Single-Precision:
  32-bit
  1 sign bit, 8 exponent bits, 23 fraction bits
  bias = 127
Double-Precision:
  64-bit
  1 sign bit, 11 exponent bits, 52 fraction bits
  bias = 1023
Floating-Point Precision

## Slide 76
Overflow: number too large to be represented
Underflow: number too small to be represented
Rounding modes:
  Down
  Up
  Toward zero
  To nearest
Example: round 1.100101 (1.578125) to only 3 fraction bits
  Down: 1.100
  Up: 1.101
  Toward zero: 1.100
  To nearest: 1.101 (1.625 is closer to 1.578125 than 1.5 is)
Floating-Point: Rounding

## Slide 77
Extract exponent and fraction bits
Prepend leading 1 to form mantissa
Compare exponents
Shift smaller mantissa if necessary
Add mantissas
Normalize mantissa and adjust exponent if necessary
Round result
Assemble exponent and fraction back into floating-point format
Floating-Point Addition

## Slide 78
Add the following floating-point numbers:
0x3FC00000
0x40500000
Floating-Point Addition Example

## Slide 79
1. Extract exponent and fraction bits
For first number (N1): S = 0, E = 127, F = .1
For second number (N2): S = 0, E = 128, F = .101
2. Prepend leading 1 to form mantissa
N1: 1.1
N2: 1.101
Floating-Point Addition Example

## Slide 80
3. Compare exponents
127 – 128 = -1, so shift N1 right by 1 bit
4. Shift smaller mantissa if necessary
shift N1’s mantissa: 1.1 >> 1 = 0.11 (× 21)
5. Add mantissas
0.11 × 21
+ 1.101 × 21
10.011 × 21
Floating-Point Addition Example

## Slide 81
6. Normalize mantissa and adjust exponent if necessary
10.011 × 21 = 1.0011 × 22
7. Round result
No need (fits in 23 bits)
8. Assemble exponent and fraction back into floating-point format
S = 0, E = 2 + 127 = 129 = 100000012, F = 001100..
in hexadecimal: 0x40980000
Floating Point Addition Example

## Slide 82
Increments on each clock edge
Used to cycle through numbers. For example,
  000, 001, 010, 011, 100, 101, 110, 111, 000, 001…
Example uses:
  Digital clock displays
  Program counter: keeps track of current instruction executing
Counters

## Slide 83
module counter (input logic clk, reset,
output logic [N-1:0] q);
logic [N-1:0] nextq;
// register
always_ff @(posedge clk, posedge reset)
if (reset) q <= 0;
else q <= nextq;
// next state
assign nextq = q + 1;
endmodule
Counter Verilog (FSM style)

## Slide 84
module counter (input logic clk, reset,
output logic [N-1:0] q);
always_ff @(posedge clk, posedge reset)
if (reset) q <= 0;
else q <= q+1;
endmodule
Counter Verilog (better idiom)

## Slide 85
Most significant bit of an N-bit counter toggles every 2N cycles.
Useful for slowing a clock. Ex: blink an LED
Example: 50 MHz clock, 24-bit counter
  2.98 Hz
Divide-by-2N Counter

## Slide 86
N-bit counter
Add p on each cycle, instead of 1
Most significant bit toggles at fout = fclk * p / 2N
Example: fclk = 50 MHz clock
  How to generate a fout = 200 Hz signal?
  p/2N = 200 / 50 MHz
Try N = 24, p = 67  fout = 199.676 Hz
Or N = 32, p = 17179  fout = 199.990 Hz
Digitally Controlled Oscillator

## Slide 87
Implementation:
Shift a new bit in on each clock edge
Shift a bit out on each clock edge
Serial-to-parallel converter: converts serial input (Sin) to parallel output (Q0:N-1)
Shift Registers
Symbol:

## Slide 88
When Load = 1, acts as a normal N-bit register
When Load = 0, acts as a shift register
Now can act as a serial-to-parallel converter (Sin to Q0:N-1) or a parallel-to-serial converter (D0:N-1 to Sout)
Shift Register with Parallel Load

## Slide 89
module shiftreg(input logic clk,
input logic load, sin,
input logic [N-1:0] d,
output logic [N-1:0] q,
output logic sout);
always_ff @(posedge clk)
if (load) q <= d;
else q <= {q[N-2:0], sin};
assign sout = q[N-1];
endmodule
Shift Register Verilog Idiom

## Slide 90
Efficiently store large amounts of data
3 common types:
  Dynamic random access memory (DRAM)
  Static random access memory (SRAM)
  Read only memory (ROM)
M-bit data value read/ written at each unique N-bit address
Memory Arrays

## Slide 91
2-dimensional array of bit cells
Each bit cell stores one bit
N address bits and M data bits:
  2N rows and M columns
  Depth: number of rows (number of words)
  Width: number of columns (size of word)
  Array size: depth × width = 2N × M
Memory Arrays

## Slide 92
22 × 3-bit array
Number of words: 4
Word size: 3-bits
For example, the 3-bit word stored at address 10 is 100
Memory Array Example

## Slide 93
Memory Arrays

## Slide 94
Memory Array Bit Cells

## Slide 95
0
1
Z
Z
Memory Array Bit Cells

## Slide 96
Wordline:
  like an enable
  single row in memory array read/written
  corresponds to unique address
  only one wordline HIGH at once
Memory Array

## Slide 97
Random access memory (RAM): volatile
Read only memory (ROM): nonvolatile
Types of Memory

## Slide 98
Volatile: loses its data when power off
Read and written quickly
Main memory in your computer is RAM (DRAM)
Historically called random access memory because any data word accessed as easily as any other (in contrast to sequential access memories such as a tape recorder)
RAM: Random Access Memory

## Slide 99
Nonvolatile: retains data when power off
Read quickly, but writing is impossible or slow
Flash memory in cameras, thumb drives, and digital cameras are all ROMs
  Historically called read only memory because ROMs were written at manufacturing time or by burning fuses. Once ROM was configured, it could not be written again. This is no longer the case for Flash memory and other types of ROMs.
ROM: Read Only Memory

## Slide 100
DRAM (Dynamic random access memory)
SRAM (Static random access memory)
Differ in how they store data:
  DRAM uses a capacitor
  SRAM uses cross-coupled inverters
Types of RAM

## Slide 101
Invented DRAM in 1966 at IBM
Others were skeptical that the idea would work
By the mid-1970’s DRAM in virtually all computers
Robert Dennard, 1932 -

## Slide 102
Data bits stored on capacitor
Dynamic because the value needs to be refreshed (rewritten) periodically and after read:
  Charge leakage from the capacitor degrades the value
  Reading destroys the stored value
DRAM

## Slide 103
DRAM

## Slide 104
SRAM

## Slide 105
DRAM bit cell:
SRAM bit cell:
Memory Arrays Review

## Slide 106
module ram #(parameter N = 6, M = 32)
(input logic clk,
input logic we,
input logic [N–1:0] adr,
input logic [M–1:0] din,
output logic [M–1:0] dout);
logic [M–1:0] mem [2**N–1:0];
always_ff @(posedge clk)
if (we) mem [adr] <= din;
assign dout = mem[adr];
endmodule
HDL Example 5.6 RAM

## Slide 107
ROM: Dot Notation

## Slide 108
ROM Storage

## Slide 109
module rom(input logic [1:0] adr, output logic [2:0] dout): always_comb case(adr) 2'b00: dout = 3'b011; 2'b01: dout = 3'b110; 2'b10: dout = 3'b100; 2'b11: dout = 3'b010; endcase endmodule
HDL Example 5.7 ROM

## Slide 110
Types of ROMs
Type | Name | Description
ROM | Read Only Memory | Chip is hardwired with presence or absence of transistors. Changing requires building a new chip.
PROM | Programmable ROM | Fuses in series with each transistor are blown to program bits. Can’t be changed after programming.
EPROM | Electrically Programmable ROM | Charge is stored on a floating gate to activate or deactivate transistor. Erasing requires exposure to UV light.
EEPROM | Electrically Erasable Programmable ROM | Like EPROM, but erasing can be done electrically.
Flash | Flash Memory | Like EEPROM, but erasing is done on large blocks to amortize cost of erase circuit. Low cost per bit, dominates nonvolatile storage today.

## Slide 111
Developed memories and high speed circuits at Toshiba, 1971-1994
Invented Flash memory as an unauthorized project pursued during nights and weekends in the late 1970’s
The process of erasing the memory reminded him of the flash of a camera
Toshiba slow to commercialize the idea; Intel was first to market in 1988
Flash has grown into a $25 billion per year market
Fujio Masuoka, 1944 -

## Slide 112
Data2 = A1 ^ A0
Data1 = A1 + A0
Data0 = A1A0
ROM Logic

## Slide 113
Implement the following logic functions using a 22 × 3-bit ROM:
  X = AB
  Y = A + B
  Z = A B
Example: Logic with ROMs

## Slide 114
Implement the following logic functions using a 22 × 3-bit ROM:
  X = AB
  Y = A + B
  Z = A B
Example: Logic with ROMs

## Slide 115
Data2 = A1 Å A0
Data1 = A1 + A0
Data0 = A1A0
Logic with Any Memory Array

## Slide 116
Implement the following logic functions using a 22 × 3-bit memory array:
  X = AB
  Y = A + B
  Z = A B
Logic with Memory Arrays

## Slide 117
Implement the following logic functions using a 22 × 3-bit memory array:
  X = AB
  Y = A + B
  Z = A B
Logic with Memory Arrays

## Slide 118
Called lookup tables (LUTs): look up output at each input combination (address)
Logic with Memory Arrays

## Slide 119
Port: address/data pair
3-ported memory
  2 read ports (A1/RD1, A2/RD2)
  1 write port (A3/WD3, WE3 enables writing)
Register file: small multi-ported memory
Multi-ported Memories

## Slide 120
// 256 x 64 memory module with one read/write port
module dmem(input logic clk, we,
input logic [7:0] a,
input logic [63:0] wd,
output logic [63:0] rd);
logic [63:0] RAM[255:0];
always @(posedge clk)
begin
rd <= RAM[a]; // synchronous read
if (we)
RAM[a] <= wd; // synchronous write
end
endmodule
SystemVerilog Memory Arrays

## Slide 121
// 16 x 32 register file with two read, 1 write port
module rf(input logic clk, we3,
input logic [3:0] a1, a2, a3,
input logic [31:0] wd3,
output logic [31:0] rd1, rd2);
logic [31:0] RAM[15:0];
always @(posedge clk) // synchronous write
if (we3)
RAM[a3] <= wd3;
assign rd1 = RAM[a1]; // asynchronous read
assign rd2 = RAM[a2];
endmodule
SystemVerilog Register File

## Slide 122
PLAs (Programmable logic arrays)
  AND array followed by OR array
  Combinational logic only
  Fixed internal connections
FPGAs (Field programmable gate arrays)
  Array of Logic Elements (LEs)
  Combinational and sequential logic
  Programmable internal connections
Logic Arrays

## Slide 123
X = ABC + ABC
Y = AB
PLAs

## Slide 124
PLAs: Dot Notation

## Slide 125
Composed of:
  LEs (Logic elements): perform logic
  IOEs (Input/output elements): interface with outside world
  Programmable interconnection: connect LEs and IOEs
  Some FPGAs include other building blocks such as multipliers and RAMs
FPGA: Field Programmable Gate Array

## Slide 126
General FPGA Layout

## Slide 127
Composed of:
  LUTs (lookup tables): perform combinational logic
  Flip-flops: perform sequential logic
  Multiplexers: connect LUTs and flip-flops
LE: Logic Element

## Slide 128
Altera Cyclone IV LE

## Slide 129
The Altera Cyclone IV LE has:
  1 four-input LUT
  1 registered output
  1 combinational output
Altera Cyclone IV LE

## Slide 130
Show how to configure a Cyclone IV LE to perform the following functions:
  X = ABC + ABC
  Y = AB
LE Configuration Example

## Slide 131
Show how to configure a Cyclone IV LE to perform the following functions:
  X = ABC + ABC
  Y = AB
LE Configuration Example

## Slide 132
How many LEs are required to build a 5-input AND gate?
Solution: 2. First performs AND4 (function of 4 variables). Second performs AND2 of the first result and the 5th input.
LE Example: AND5

## Slide 133
How many LEs are required to build a 3-bit counter?
Solution: 3. The counter has 3 flip-flops, so it requires at least 3 LEs. The add logic for each bit is a function of less than 4 variables, so it can fit in the LUT before the flop. Hence, 3 LEs is sufficient.
LE Example: 3-bit counter

## Slide 134
Using a CAD tool (such as Altera’s Quartus II)
  Enter the design with a HDL
  Simulate the design
  Synthesize design and map it onto FPGA
  Download the configuration onto the FPGA
  Test the design
FPGA Design Flow
This is an iterative process!