## Slide 1: Lab 2: Introduction to hardware description language

## Slide 2: Design flow
In this course: To design a digital circuit
Truth table
Describe hardware using HDL (SystemVerilog)
Simulate
(ModelSim)
Test on board
(STEP MAX 10) board
Synthesis
(Quartus)

## Slide 3: Simulation and Synthesis
Simulation
To verify the module operates correctly or not
By applying inputs to a module and checking outputs
Synthesis
Textual description of a module is transformed into logic gates.

## Slide 4: Hardware description language
Hardware Description Languages (HDL) like SystemVerilog are used to describe hardware
behavior
-> It can be converted to digital blocks made up of combinational and sequential elements.
SystemVerilog is an extension of Verilog with more features

## Slide 5: Module
Definition:
Module is block of SystemVerilog code that implements a certain functionality
A module can be embedded within other modules and these modules can communicate
with each other using their input + output ports.
Syntax:
module Module_name( input [data_type] port1, input [data_type] port2, output [data_type] port3);
//internal logic
endmodule
Declaration: Using module keyword, followed by module name, an optional port list; end of a module by
endmodule keyword
Portlist: Specify input, output ports to module and their data types; portlist is optional.
Internal logic: Specify how module ’s outputs are derived from its inputs: using operators, assignments, variables, statements, call other modules,…..

## Slide 6: Data types and values of a variable
Basic data types available in SystemVerilog are shown in table below:
Nearly all SystemVerilog signals can be logic, except that
signals with multiple drivers
Values SystemVerilog variables can hold
0 | represents a logic zero, or a false condition
1 | represents a logic one, or a true condition
x or X | represents an unknown logic value (can be zero or one)
z | represents a high-impedance state

## Slide 7: Operator and precedence
SystemVerilog operators and precedence of operators are shown in below table:
Some types of operators:
- Arithmetic operators
- Relational operators
- Bitwise operators
- Conditional operator
- Assignment operators
+ Blocking assignment
+ Non-blocking assignment

## Slide 8: Continuous and conditional assignment assignamn
Continuous assignment: value of the left-hand side signal is continuously updated to match the value of the right-hand side expression
assign statement is used to create continuous assignment in hardware description.
Syntax:
assign LHS = RHS
LHS: signal need to assign a value to
RHS: signal or expression
Conditional assignment: select the output from among alternatives based on an input called the condition
Using assign statement and conditional operator ?:
Syntax:
assign y= <first exp> ?: <second exp> : <third exp>
Based on value of first exp (condition) to choose second exp or third exp

## Slide 9: Example: inverter
An example of design an inverter using SystemVerilog is shown below
module inverter(input logic x,
output logic y);
assign y = ~x;
endmodule

## Slide 10: Writing testbench
Testbench: a SystemVerilog module to verify the functionality of a design through simulations.
Steps:
- Top level hardware design module is instantiated within testbench
- Declare testbench component signals and connect them to design ‘s input/output ports
- Inputs to the design are driven with certain values
- Outputs of design are analyzed and compared with expected values to check if the design behavior is correct or not

## Slide 11: Writing testbench (cont)
Structure of a testbench:
// All verification components are placed in this top testbench module
Module tb_top();
// Declare testbench component signals that need to be connected to the design instance
// These signals are assigned some values that in turn gets transferred to
// the design as inputs because they are connected with the ports in the design
logic a, b, y;
// Instantiate the design module and connect the testbench component signals declared above with the ports in the design
mydesign DUT(a,b,y);
//Assign values to testbench component signals that can be diven to the design
DUT stands for design under test and is top hardware design module written in SystemVerilog

## Slide 12: Example: inverter (cont)
An example testbench for inverter design is given below:
module inverter_tb();
logic a,b;
// instantiate device under test
inverter dut(a,b);
//apply input one at a time
initial begin
a=0; #10;
assert (b == 1) else $error(“a = 0 failed”);
a=1; #10;
assert (b == 0) else $error(“a = 1 failed”);
end
endmodule
delay:#10 – delay 10 time units
initial: define a block of code that is
execute once at the beginning of a simulation;
used for initialization, testbench setup,…
assert: a statement is used to specified and check conditions during design and verification.
$error: is used to report error message during simulation, if encounterd, $error stops simulation and displays message.

## Slide 13: Run simulation in Quaturs
After add inverter.sv and inverter_tb.sv file to current project -> run simulation
Choose Asignments -> Settings to add testbench file

## Slide 14: Run simulation in Quaturs (cont)
In Settings, go to Simulation and configure as picture below

## Slide 15: Run simulation in Quaturs (cont)
Click on TestBenches -> New
Enter test bench name, top level module in test bench
In Filename, browse to inverter_tb.sv file in your computer and click Add -> OK

## Slide 16: Run simulation in Quaturs (cont)
Add path to ModelSim: go to Tools -> Options -> EDA Tool Options -> add path to ModelSim Altera
Path has format:
C:/intelFPGA_lite/20.1std/modelsim_ase/win32aloem
Choose Tools -> Run Simulation Tool -> RTL Simulation to lauch ModelSim and observe result of simulation

## Slide 17: Test design module in STEP MAX-10 board (cont)
Go to Assignments -> Pin Planner -> assign pins of design module on DE-10 board

## Slide 18: Test design module in STEP MAX-10 board (cont)
Below table show Pin assignment on STEP MAX-10 board

## Slide 19
Do complete Compline step in design
Right click on Compile Design -> Start
All green check mark -> done Compline
Test design module in STEP MAX-10 board (cont)

## Slide 20: Test design module in STEP MAX-10 board (cont)
Go to Tool -> Programmer
After select Hardware , click on Start
Progress bar is full with green -> Done
Check operations of design on DE-10 board

## Slide 21: Exercises
Ex1: Design a NAND gate using SystemVerilog, simulate on ModelSim and test operations of design in STEP MAX-10 board.
Ex2: Design a 2:1 multiplexer using SystemVerilog, simulate on ModelSim and test operations of design in STEP MAX-10 board. (Using conditional operator)
Ex3: Design a 4:1 multiplexer using SystemVerilog, simulate on ModelSim and test operations of design in STEP MAX-10 board. (Using conditional operator)